## Slide 1
Individual Tree Segmentation from Handheld LiDAR Point Clouds for DBH Estimation in Rubber Plantations using Multi-channel CNN
Draft Thesis Proposal
[Student Name] [Student ID]
Advisor: [Advisor Name]
Department of Computer Engineering, Chulalongkorn University
1

## Slide 2
Motivation
Forest inventory needs reliable tree-level measurements.
Diameter at breast height (DBH) is a core variable for forest inventory, biomass estimation, and growth monitoring.
Manual DBH measurement is accurate but labor-intensive, especially across repeated surveys and multiple plots.
Handheld LiDAR can rapidly capture 3D understory structure around tree stems.
The bottleneck is robust individual tree segmentation before downstream DBH extraction.
2

## Slide 3
Problem Statement
From 12 rubber plantation point clouds to individual trees and DBH.
Input: 12 handheld/mobile LiDAR point clouds from rubber plantation plots.
Ground truth: tree locations and DBH measurements for each plot.
Output: tree-level detections or segments, then DBH estimated from points near breast height.
Challenges include uneven point density, occlusion, understory clutter, and regularly spaced stems that may be merged.
3

## Slide 4
Related Work Landscape
Most systems combine segmentation, stem mapping, and geometric fitting.
Classical pipelines rely on ground filtering, trunk extraction, clustering, and circle or cylinder fitting.
Mobile and handheld LiDAR DBH systems track individual trees and fit trunk models from accumulated scans.
Large-scale MLS inventory uses semantic segmentation, stem mapping, and DBH measurement at the individual-tree level.
TreeLearn performs 3D point-cloud tree instance segmentation using sparse convolutional neural networks.
TreeScope and SLOAM provide robotics-oriented LiDAR datasets and mapping frameworks for tree inventory tasks.
4

## Slide 5
Research Gap
There is an accuracy-efficiency gap between lightweight 2D models and heavy 3D point-cloud models.
Rule-based point-cloud methods are sensitive to radius, density, voxel size, and fitting thresholds.
DBH errors often originate from poor segmentation, occluded stems, incomplete breast-height slices, or branch/leaf contamination.
TreeLearn is powerful but requires 3D sparse CNN inference, GPU memory, and possibly domain fine-tuning.
A single-channel top-view density image is lightweight but discards vertical structure and breast-height evidence.
It remains unclear whether physically meaningful multi-channel 2D features can improve accuracy while preserving efficiency.
5

## Slide 6
Research Objectives
The proposal focuses on individual tree segmentation as the upstream step for DBH estimation.
Develop a multi-channel CNN pipeline for individual tree segmentation from handheld LiDAR point clouds.
Compare multi-channel CNN with a single-channel density baseline using the same plantation plots.
Benchmark against 3D point-cloud-based methods such as TreeLearn on the same test data.
Quantify how segmentation quality affects downstream DBH extraction accuracy.
Evaluate runtime, memory/VRAM usage, model size, and deployment practicality.
6

## Slide 7
Research Questions
Key questions and working hypotheses.
RQ1: Does multi-channel CNN improve precision, recall, and F1-score over a density-only baseline?
RQ2: How close is multi-channel CNN to TreeLearn when both are evaluated on the same rubber plantation plots?
RQ3: Does multi-channel CNN reduce inference time and resource usage compared with 3D point-cloud segmentation?
H1: Height-above-ground and breast-height density channels reduce false positives and false negatives.
H2: Better individual tree segmentation reduces downstream DBH error.
7

## Slide 8
Dataset and Controls
Rubber plantation data will be evaluated at the plot level.
Main dataset: 12 rubber plantation point clouds.
Labels: tree X/Y positions and field-measured DBH from CSV files.
Preprocessing: PCD/LAS conversion, filtering, rotation, and coordinate alignment with labels.
Train/validation/test split will be performed by plot to prevent leakage.
The same split seed, image size, pixel size, bounding-box size, and augmentation policy will be used for fair comparison.
8

## Slide 9
Proposed System Overview
Multi-channel CNN is used for individual tree segmentation before DBH fitting.
Point cloud
Feature raster
CNN/YOLO
Tree crop
DBH fitting
Metrics
Point cloud preprocessing normalizes the plot and aligns coordinates.
Feature rasterization converts 3D points into physically meaningful 2D channels.
CNN/YOLO predicts tree centers or tree-level regions in top-view space.
Predicted trees are used to crop trunk points near breast height.
DBH is estimated using circle/cylinder fitting and compared with field measurements.
9

## Slide 10
Multi-channel CNN Input
Synthetic RGB channels encode LiDAR-derived physical features.
R = density: number of points in each top-view grid cell.
G = hag_p95: 95th percentile of height above local ground in each cell.
B = dbh_band_density: number of points in the 1.0-1.6 m height-above-ground band.
The representation reuses the existing CNN/YOLO workflow without changing the input layer.
Color augmentation is disabled because channel colors represent physical features, not natural image color.
10

## Slide 11
Comparison Methods
All methods will be evaluated on the same test plots.
Single-channel CNN: top-view density image and YOLO/CNN detector.
Proposed multi-channel CNN: density + height-above-ground + breast-height density.
TreeLearn: 3D sparse CNN tree instance segmentation directly on point clouds.
Point-cloud baseline: ground filtering, trunk extraction, clustering, and circle/cylinder fitting.
Optional references: SLOAM and TreeScope-style metrics for stem mapping and diameter estimation.
11

## Slide 12
Experiment Design
The experiments isolate representation quality, model accuracy, and efficiency.
Experiment 1: density-only CNN versus multi-channel CNN.
Experiment 2: channel ablation: density, density + hag_p95, density + dbh_band_density, and all channels.
Experiment 3: multi-channel CNN versus TreeLearn on identical test plots.
Experiment 4: DBH extraction from each method using single-slice and multi-height-bin fitting.
Experiment 5: runtime and resource benchmark for preprocessing, inference, and DBH fitting.
12

## Slide 13
Evaluation Metrics
Accuracy and efficiency will be reported separately.
Tree detection: precision, recall, F1-score, tree detection rate, and plot-level count error.
Localization: matched center error, omission error, and commission error.
Instance quality: coverage, IoU, or point-level metrics if point-level instance labels are available.
DBH extraction: MAE, RMSE, bias, relative error, and percentage of trees within +/- 2 cm or +/- 5 cm.
Efficiency: runtime per plot, peak CPU memory, peak GPU memory, throughput, and model size.
13

## Slide 14
Expected Contributions
The study aims to deliver a practical accuracy-efficiency benchmark.
A reproducible pipeline for rubber-tree segmentation and DBH extraction from handheld LiDAR point clouds.
A multi-channel raster representation that preserves useful vertical and breast-height information.
A controlled benchmark comparing density-only CNN, multi-channel CNN, TreeLearn, and point-cloud baselines.
An analysis of how segmentation errors propagate into DBH estimation errors.
Practical guidance on when lightweight 2D multi-channel CNN is preferable to direct 3D point-cloud segmentation.
14

## Slide 15
References: Individual Tree Segmentation
Grouped references follow the same numbered style used in the example proposal.
[1] Liu, Lulu, Aiwu Zhang, Shen Xiao, Shaoxing Hu, Nianpeng He, Haiyang Pang, Xizhen Zhang, and Shikai Yang. 2021. "Single Tree Segmentation and Diameter at Breast Height Estimation With Mobile LiDAR." IEEE Access 9: 24314-24325.
[2] Henrich, Jonathan, Jan van Delden, Dominik Seidel, Thomas Kneib, and Alexander S. Ecker. 2024. "TreeLearn: A Deep Learning Method for Segmenting Individual Trees from Ground-Based LiDAR Forest Point Clouds." Ecological Informatics 84: 102888.
[3] Shao, Jinyuan, Yi-Chun Lin, Cameron Wingren, Sang-Yeop Shin, William Fei, Joshua Carpenter, Ayman Habib, and Songlin Fei. 2024. "Large-Scale Inventory in Natural Forests with Mobile LiDAR Point Clouds." Science of Remote Sensing 10: 100168.
[4] Li, Qiujie, and Yu Yan. 2024. "Street Tree Segmentation from Mobile Laser Scanning Data Using Deep Learning-Based Image Instance Segmentation." Urban Forestry & Urban Greening 92: 128200.
[5] Cheng, Derek, Fernando Cladera Ojeda, Ankit Prabhu, Xu Liu, Alan Zhu, Patrick Corey Green, Reza Ehsani, Pratik Chaudhari, and Vijay Kumar. 2023. "TreeScope: An Agricultural Robotics Dataset for LiDAR-Based Mapping of Trees in Forests and Orchards." arXiv:2310.02162.
15

## Slide 16
References: DBH Extraction
DBH-focused references are separated from segmentation references.
[1] Proudman, Alexander, Milad Ramezani, and Maurice Fallon. 2021. "Online Estimation of Diameter at Breast Height (DBH) of Forest Trees Using a Handheld LiDAR." 2021 European Conference on Mobile Robots (ECMR).
[2] Sheng, Yuhao, Qingzhan Zhao, Xuewen Wang, Yihao Liu, and Xiaojun Yin. 2024. "Tree Diameter at Breast Height Extraction Based on Mobile Laser Scanning Point Cloud." Forests 15 (4): 590.
[3] Liu, Lulu, Aiwu Zhang, Shen Xiao, Shaoxing Hu, Nianpeng He, Haiyang Pang, Xizhen Zhang, and Shikai Yang. 2021. "Single Tree Segmentation and Diameter at Breast Height Estimation With Mobile LiDAR." IEEE Access 9: 24314-24325.
[4] Shao, Jinyuan, Yi-Chun Lin, Cameron Wingren, Sang-Yeop Shin, William Fei, Joshua Carpenter, Ayman Habib, and Songlin Fei. 2024. "Large-Scale Inventory in Natural Forests with Mobile LiDAR Point Clouds." Science of Remote Sensing 10: 100168.
[5] Cheng, Derek, Fernando Cladera Ojeda, Ankit Prabhu, Xu Liu, Alan Zhu, Patrick Corey Green, Reza Ehsani, Pratik Chaudhari, and Vijay Kumar. 2023. "TreeScope: An Agricultural Robotics Dataset for LiDAR-Based Mapping of Trees in Forests and Orchards." arXiv:2310.02162.
16